## Slide 1
ANALOG-TO-DIGITAL CONVERSION
change an analog signal to digital data. In this section we describe two techniques, pulse code modulation and delta modulation.
Pulse Code Modulation (PCM) Delta Modulation (DM)
Topics discussed in this section:

## Slide 2
Figure 4.21 Components of PCM encoder

## Slide 3
Figure 4.22 Three different sampling methods for PCM

## Slide 4
According to the Nyquist theorem, the sampling rate must be
at least 2 times the highest frequency contained in the signal.
Note

## Slide 6
Figure 4.26 Quantization and encoding of a sampled signal

## Slide 7
We want to digitize the human voice. What is the bit rate, assuming 8 bits per sample?
Solution
The human voice normally contains frequencies from 0 to 4000 Hz. So the sampling rate and bit rate are calculated as follows:
Example 4.14

## Slide 8
Figure 4.27 Components of a PCM decoder

## Slide 9: Delta Modulation
PCM finds the value of signal amplitude for each signal.
DM finds the change from the previous sample

## Slide 10
Figure 4.29 Delta modulation components

## Slide 11
The process of delta modulation

## Slide 12
Figure 4.30 Delta demodulation components

## Slide 13
4-3 TRANSMISSION MODES
The transmission of binary data across a link can be accomplished in either parallel or serial mode. In parallel mode, multiple bits are sent with each clock tick. In serial mode, 1 bit is sent with each clock tick. While there is only one way to send parallel data, there are three subclasses of serial transmission: asynchronous, synchronous, and isochronous.
Parallel Transmission Serial Transmission
Topics discussed in this section:

## Slide 14
Figure 4.31 Data transmission and modes

## Slide 15
Figure 4.32 Parallel transmission

## Slide 16
Figure 4.33 Serial transmission

## Slide 17
In asynchronous transmission, we send 1 start bit (0) at the beginning and 1 or more stop bits (1s) at the end of each byte. There may be a gap between each byte.
Note

## Slide 18
Asynchronous here means “asynchronous at the byte level,”
but the bits are still synchronized; their durations are the same.
Note

## Slide 19
Figure 4.34 Asynchronous transmission

## Slide 20
In synchronous transmission, we send bits one after another without start or stop bits or gaps. It is the responsibility of the receiver to group the bits.
Note

## Slide 21
Figure 4.35 Synchronous transmission

## Slide 22
Chapter 4
Digital Transmission
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.