## Slide 1
LINEAR BLOCK CODES
Almost all block codes used today belong to a subset called linear block codes. A linear block code is a code in which the exclusive OR (addition modulo-2) of two valid codewords creates another valid codeword.
Minimum Distance for Linear Block Codes Some Linear Block Codes
Topics discussed in this section:

## Slide 2
In a linear block code, the exclusive OR (XOR) of any two valid codewords creates another valid codeword.
Note

## Slide 3
Table 10.1

## Slide 4
Table 10.2

## Slide 5
Let us see if the two codes we defined in Table 10.1 and Table 10.2 belong to the class of linear block codes.
1. The scheme in Table 10.1 is a linear block code because the result of XORing any codeword with any other codeword is a valid codeword. For example, the XORing of the second and third codewords creates the fourth one.
2. The scheme in Table 10.2 is also a linear block code. We can create all four codewords by XORing two other codewords.
Example 10.10

## Slide 6
In our first code (Table 10.1), the numbers of 1s in the nonzero codewords are 2, 2, and 2. So the minimum Hamming distance is dmin = 2. In our second code (Table 10.2), the numbers of 1s in the nonzero codewords are 3, 3, and 4. So in this code we have dmin = 3.
Example 10.11

## Slide 7
A simple parity-check code is a single-bit error-detecting code in which n = k + 1 with dmin = 2.
Note

## Slide 8
Table 10.3 Simple parity-check code C(5, 4)

## Slide 9
Figure 10.10 Encoder and decoder for simple parity-check code

## Slide 10
Let us look at some transmission scenarios. Assume the sender sends the dataword 1011. The codeword created from this dataword is 10111, which is sent to the receiver. We examine five cases:
1. No error occurs; the received codeword is 10111. The syndrome is 0. The dataword 1011 is created.
2. One single-bit error changes a1 . The received codeword is 10011. The syndrome is 1. No dataword is created.
3. One single-bit error changes r0 . The received codeword is 10110. The syndrome is 1. No dataword is created.
Example 10.12

## Slide 11
4. An error changes r0 and a second error changes a3 .
The received codeword is 00110. The syndrome is 0. The dataword 0011 is created at the receiver. Note that
here the dataword is wrongly created due to the
syndrome value.
5. Three bits—a3, a2, and a1—are changed by errors. The received codeword is 01011. The syndrome is 1. The dataword is not created. This shows that the simple parity check, guaranteed to detect one single error, can also find any odd number of errors.
Example 10.12 (continued)

## Slide 12
A simple parity-check code can detect an odd number of errors.
Note

## Slide 13
All Hamming codes discussed have dmin = 3.
The relationship between m and n in these codes is n = 2m − 1.
Note

## Slide 14
Figure 10.11 Two-dimensional parity-check code

## Slide 15
Figure 10.11 Two-dimensional parity-check code

## Slide 16
Figure 10.11 Two-dimensional parity-check code

## Slide 17
Table 10.4 Hamming code C(7, 4)

## Slide 18
Figure 10.12 The structure of the encoder and decoder for a Hamming code

## Slide 19
Table 10.5 Logical decision made by the correction logic analyzer

## Slide 20
Let us trace the path of three datawords from the sender to the destination:
1. The dataword 0100 becomes the codeword 0100011. The codeword 0100011 is received. The syndrome is 000, the final dataword is 0100.
2. The dataword 0111 becomes the codeword 0111001. The syndrome is 011. After flipping b2 (changing the 1 to 0), the final dataword is 0111.
3. The dataword 1101 becomes the codeword 1101000. The syndrome is 101. After flipping b0, we get 0000, the wrong dataword. This shows that our code cannot correct two errors.
Example 10.13

## Slide 21
Figure 10.13 Burst error correction using Hamming code

## Slide 22
References:
Chapter 10
Error Detection and Correction
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.