## Slide 2: TRANSMISSION IMPAIRMENTS (1)
signal that is received may differ from the signal that is transmitted due to various transmission impairments.
For analog signals, these impairments can degrade the signal quality.
For digital signals, bit errors may be introduced, such that a binary 1 is transformed into a binary 0 or vice versa.

## Slide 3: TRANSMISSION IMPAIRMENTS (2)
The most significant impairments are
• Attenuation and attenuation distortion
• Delay distortion
• Noise

## Slide 4: TRANSMISSION IMPAIRMENTS (3)
Attenuation and attenuation distortion
The strength of a signal falls off with distance over any transmission medium.
guided media: reduction in strength, or attenuation, is generally exponential and thus is typically expressed as a constant number of decibels per unit distance.
unguided media: attenuation is a more complex function of distance and the makeup of the atmosphere.
Attenuation introduces three considerations for the transmission engineer.
a received signal must have sufficient strength so that the electronic circuitry in the receiver can detect the signal.
the signal must maintain a level sufficiently higher than noise to be received without error.
attenuation varies with frequency.

## Slide 5: TRANSMISSION IMPAIRMENTS (4)
Attenuation and attenuation distortion
The first and second problems are dealt with by attention to signal strength and the use of amplifiers or repeaters.
For a point-to-point link, the signal strength of the transmitter must be strong enough to be received intelligibly, but not so strong as to overload the circuitry of the transmitter or receiver, which would cause distortion.

## Slide 6: TRANSMISSION IMPAIRMENTS (5)
Attenuation and attenuation distortion
These problems are more complex for multipoint lines where the distance from transmitter to receiver is variable.
The third problem is particularly noticeable for analog signals because the attenuation varies as a function of frequency, the received signal is distorted, reducing intelligibility.
To overcome this problem, techniques are used for equalizing attenuation across a band of frequencies.

## Slide 7: TRANSMISSION IMPAIRMENTS (6)
Delay Distortion
Delay distortion occurs because the velocity of propagation of a signal through a guided medium varies with frequency.
For a bandlimited signal, the velocity tends to be highest near the center frequency and fall off toward the two edges of the band.
Thus various frequency components of a signal will arrive at the receiver at different times, resulting in phase shifts between the different frequencies.
This effect is referred to as delay distortion because the received signal is distorted due to varying delays experienced at its constituent frequencies.

## Slide 8: TRANSMISSION IMPAIRMENTS (7)
Delay Distortion
Delay distortion is particularly critical for digital data.
Consider that a sequence of bits is being transmitted, using either analog or digital signals.
Because of delay distortion, some of the signal components of one bit position will spill over into other bit positions, causing intersymbol interference, which is a major limitation to maximum bit rate over a transmission channel.

## Slide 9: TRANSMISSION IMPAIRMENTS (8)
Noise
For any data transmission event, the received signal will consist of
  the transmitted signal, modified by the various distortions imposed by the transmission system,
  Plus additional unwanted signals that are inserted somewhere between transmission and reception.
These undesired signals are referred to as noise.
Noise is the major limiting factor in communications system performance.
Noise may be divided into four categories:
  Thermal noise
  Intermodulation noise
  Crosstalk
  Impulse noise

## Slide 10: TRANSMISSION IMPAIRMENTS (9)
Noise
Thermal noise : due to thermal agitation of electrons.
present in all electronic devices and transmission media and is a function of temperature.
uniformly distributed across the bandwidths typically used in communications systems and hence is often referred to as white noise.
Thermal noise cannot be eliminated and therefore places an upper bound on communications system performance.

## Slide 11: TRANSMISSION IMPAIRMENTS (10)
Noise
Intermodulation noise:
When signals at different frequencies share the same transmission medium, the result may be intermodulation noise.
The effect of intermodulation noise is to produce signals at a frequency that is the sum or difference of the two original frequencies or multiples of those frequencies.
For example, the mixing of signals at frequencies f1 and f2 might produce energy at the frequency f1+f2.
This derived signal could interfere with an intended signal at the frequency f1+f2.

## Slide 12: TRANSMISSION IMPAIRMENTS (11)
Noise
Crosstalk
It is an unwanted coupling between signal paths.
It can occur by electrical coupling between nearby twisted pairs or, rarely, coax cable lines carrying multiple signals.
Crosstalk can also occur when microwave antennas pick up unwanted signals; although highly directional antennas are used, microwave energy does spread during propagation.
Typically, crosstalk is of the same order of magnitude as, or less than, thermal noise.

## Slide 13: TRANSMISSION IMPAIRMENTS (12)
Noise
Impulse noise:
Non-continuous, consisting of irregular pulses or noise spikes of short duration and of relatively high amplitude.
Generated from a variety of causes, including external electromagnetic disturbances, such as lightning, and faults and flaws in the communications system.
Impulse noise is generally only a minor annoyance for analog data.
For example, voice transmission may be corrupted by short clicks and crackles with no loss of intelligibility.
However, impulse noise is the primary source of error in digital data communication.

## Slide 14: CHANNEL CAPACITY (1)
The maximum rate at which data can be transmitted over a given communication path, or channel, under given conditions
There are four concepts here that we are trying to relate to one another.
• Data rate: The rate, in bits per second (bps), at which data can be communicated.
Bandwidth: The bandwidth of the transmitted signal as constrained by the transmitter and the nature of the transmission medium, expressed in cycles per second, or Hertz
Noise: The average level of noise over the communications path
Error rate: The rate at which errors occur, where an error is the reception of a 1 when a 0 was transmitted or the reception of a 0 when a 1 was transmitted.

## Slide 15: CHANNEL CAPACITY (2)
The problem we are addressing is this: Communications facilities are expensive and, in general, the greater the bandwidth of a facility, the greater the cost.
Furthermore, all transmission channels of any practical interest are of limited bandwidth.
The limitations arise from the physical properties of the transmission medium or from deliberate limitations at the transmitter on the bandwidth to prevent interference from other sources.
Aim: to make as efficient use as possible of a given bandwidth.
For digital data, this means that we would like to get as high a data rate as possible at a particular limit of error rate for a given bandwidth.
The main constraint on achieving this efficiency is noise.